## Slide 1
HSMC Connector
Pin 111
(3.3V)
Pin 158
J3
R74
1 | 2 | 3
To working FMC connection
Steps to use I2C over HSMC
1. Remove resistor R74
2. Install 3 pin header H1
3. Jumper H1 pin 1 to left pad of R74*
4. Jumper H1 pin 2 to right pad of R74*
5. Jumper H1 pin 3 to pin 158 of J3 (HSMC connector)
For FMC use:
Short pins 1 and 2 of H1
For HSMC use:
Short pins 2 and 3 of H1
*Directions given relative to R74 reference designator
H1
Layout Error
Unused
HSMC pin
To I2C
SDA
pin